## Slide 1: Input Device Interrupt Latency of KVM on ARM using Passthrough
Koji Teranishi
寺西 光司
IGEL Co., Ltd.

## Slide 2: Who are you?
  Software engineer
  Recent work
    Survey around using kvm on arm
    Developping application with Qt, web languages

## Slide 3: Overview
Introduction (about KVM ,device virtualization,...)
Pareparation of environment
Implementation for measurement
Result
Case study

## Slide 4: Introduction

## Slide 5: Introduction
KVM on ARM
  KVM(Kernel-based Virtual Machine) is a kernel module that enables the kernel to run as a hypervisor
  KVM supports processor of intel, AMD, also ARM
  KVM is used with machine virtualizer like QEMU

## Slide 6: Introduction
Three types of Device virtualization
  Full virtualization
    Hypervisor provides a virtual device completely emulates a real hardware device
    Low performance by the emulation
  Paravirtualization
    Hypervisor provides a virtual device which is optimised for virtual environment
    The guest needs a device driver designed for the device
    Improve performance compare to full virtualization
  Passthrough
    Hypervisor exposes a real device to the guest exclusively
    Guest can directly use the device as if on the native environment
    Get high performance near the native environment

## Slide 7: Introduction
Some latency will occur on using passthrough, but how much is it ?
Want to measure the latency time of USB HID passthrough
The processing of virtualization can give some latency to the usb host controller
We try to measure the latency on the interrupt handler

## Slide 8: Preparation of environment

## Slide 9: Preparation of environment
Renesas R-Car M3 (R8J77960(SiP))
  Arm Cortex A-57 dual,53 quad, -R7 Dual Lock-Step
  IMG PowerVR Series6XT GX6250
  Memory controller for LPDDR4-SDRAM 32bit bus 2ch
  3 channels Display Output
  8 channels Video Input
  USB3.0 and USB2.0(OTG) interfaces
  PCI Express Interfaces

## Slide 10: Preparation of environment
We measure the interval between host controller driver’s interrupt handler of Host and Guest
The order of event step
USB Host Controller
Interrupt handler on Host
Virtualized USB Host Contorller
Interrupt handler on Guest

## Slide 11: Preparation of environment
What type of HID device should we use for sending event ?
  Want to measure the latency closely
  Process like sending many events at a regular intervals will be needed
  Want to control of the sending events by programming…
  Normal HID device (like mouse,keyboard …) is not enough
  Using the board as HID gadget is an answear (the board has USB OTG)

## Slide 12: Preparation of environment
Using two board (as HID Gadget and the Host)
The type of the gadget is mouse(enough for sending a data)

## Slide 13: Preparation of environment
Some clock is needed to measure the time
The system clock which runs on host is not common to guest’s
We need a clock which is independent from them
The board we use have a built-in hardware timer module (called TMU)

## Slide 14: Preparation of environment
Setup USB gadget
  Need to enable HID Gadget on kernel config of USB gadget kernel
  or enable below parameters
  CONFIG_USB_GADGET=y
  CONFIG_USB_F_HID=y
  CONFIG_USB_G_HID=y
  USB_LIBCOMPOSITE=y

## Slide 15: Preparation of environment
Setup USB gadget
  Write a script to setup a simple HID mouse gadget
  https://github.com/qlyoung/keyboard-gadget is useful
  Run the scrupt
  If it succeeds , we can find the device file /dev/hidg0 !
Replace UDC driver name at /sys/class/udc/
#!/bin/bash
PROTOCOL=2
SUBCLASS=1
REPORT_LENGTH=8
UDC=e6590000.usb
…

## Slide 16: Implementation for measurement

## Slide 17: Implementation for measurement
Kernel
  The USB host controller driver need to handle TMU when a interruption happens
  On the Host, it resets and starts the timer
  On the Guest, it gets the time and output the result by printk

## Slide 18: Implementation for measurement
QEMU(virtual machine emulater)
  Memory mapping is needed to show host’s TMU register to guest
  Add a virtual device which do the mapping to qemu code
  The file hw/misc/exynos4210_pmu.c was helpful
The example of memory mapping part
int fd = open("/dev/mem", O_RDWR|O_SYNC);
mapped_addr = mmap( …, fd, the offset we’ll access);
memory_region_init_ram_ptr(region, … , device_name, region_size, mapped_addr);
memory_region_add_subregion(get_system_memory(), … , region);
We’ll set TMU’s

## Slide 19: Implementation for measurement
What we need for script of starting QEMU
  USB host controller
  Host device to be passed
  Virtual device we made
qemu-system-aarch64 \
...
-device nec-usb-xhci,id=xhci \
-device usbhost,hostbus=1,hostport=1.3 \
-device device_name
The bus and port information can be found by “lsusb -t” command

## Slide 20: Implementation for measurement
Program sending event
  Open the gadget device file(/dev/hidg0)
  Write a event data to the fd
If the program start …
  The results can be shown by “dmesg”
  “dmesg -w” will follow the messages continually
  Redirect the result to a file

## Slide 21: Result

## Slide 22: Result
The result of sending 10000 times with 10ms intervals
Almost around 100 ~400
Very small amont is high latency

## Slide 23: Result
The histogram of the frequency with 50 usec intervals
150~200 is highest frequency

## Slide 24: Case study

## Slide 25: Case study
Examined the latency of one direction(host -> guest)
How about it containing reverse(guest -> host)?
How to measure
  Try to measure the latency on using keyboard
  By pressing CapsLock, we get feedback to turn on/off LED
  Measure the roundtrip time
  Compare the result of host(no virtualization) to guest

## Slide 26: Case study
Preparation
  Same environment to previous one but use HID Keyboard as gadget
Detail
  Send a key data at a regular intervals
  Wait until getting feedback
  Measure the roundtrip time by using clock_gettime function

## Slide 27: Case study
Result – Sending 500 times every 1 second
About 1ms later than host

## Slide 28: Conclusion

## Slide 29: Conclusion
The latency between interrupt handlers was almost 100 ~200 usec
It was not significant latency in the case of HID device
The result of roundtrip seems to be affected by USB host polling to device every 1ms on HID

## Slide 30: Title